Modern Digital Modulation Techniques

ELEN E6909

Columbia University

Spring Semester- 2008

Extra Figures on OFDM

20 April 2008

Professor I. Kalet

“Mobile” Wi-Max

(Scalable OFDMA-SOFDMA)

(Wi-Max Forum –2006)

Channel 				1.25		  5	        10           20

Bandwidth (MHz)

Sampling Frequency		1.4 		5.6 	      11.2       22.4

(Msamples/sec)

FFT-Size 				128 	        512 	     1024       2048

Number of Subchannels	   2 		  8 		16	      32

Subcarrier Spacing 					10.94 kHz

Useful Symbol Time  				  91.4 (s

Guard Time   						  11.4 (s

Total Symbol Time  					102.9 (s

Number of OFDMA  				  48

Symbols  (5 ms Frame)

3G Long-Term Evolution (LTE)

H. Ekstrom, A. Furuskar, J. Karlsonn, M. Speyer, S. Parkvall, J. Torsner and M. Wahlqvist, “Technical solutions for the 3G long-term evolution, IEEE Communications Magazine, March 2006, pp. 38-45.

##### Downlink-OFDMA

##### -2048 Frequencies

##### -Tone Spacing-15 kHz

-QPSK, 16-QAM and 64-QAM

-Bandwidths- 1.25, 2.5, 5, 10, 15

and 20 MHz

-Subframes-minimum time = .5ms

-Radio Frame=10 ms

##### Uplink-Single-Tone FDMA

##### -Reduce Peak-to-Average

##### -Use Frequency Domain Equalization

-Can change bandwidth of QAM signal

3G-LTE

Available Downlink Bandwidth –Physical Resource Blocks

Bandwidth (MHz) 		1.25 	 2.5 	 5 	10	15	 20

Subcarrier Bandwidth 	    	    15 kHz

Physical Resource Block 		    180 kHz

(PRB)Bandwidth                       (12 x15 kHz)

Number of Available 	 6 	 12 	25 	50 	75    100

PRBs

# Twelve subcarriers x 15 kHz per subcarrier= 180 kHz

(One Time-Slot= .5 ms)

##### Downlink-OFDMA

##### Unicast Scenario

##### 4.7 (s ((4700 feet (1.3 km)

##### 1/15 kHz

(66.7 (s)

##### 71.4 (s

##### OFDM Block

##### -Seven OFDM Blocks in One .5 ms subframe

##### (7 x 71.4 (s =500.19 (s)

##### Multicast (Broadcasting) Scenario

##### 16.7 (s ((16700 feet ( 5 km)

##### 1/15 kHz

(66.7 (s)

##### 82.4 (s

##### OFDM Block

##### -Six OFDM Blocks in One .5 ms subframe

##### (6 x 82.4 (s =494 (s)

3G Long Term Evolution (LTE)

One .5 ms Subframe

##### Unicast Scenario  (seven ODFM blocks)

##### 71.4 (s

##### .5 ms

##### Multicast Scenario  (six ODFM blocks)

##### 82.4 (s

.5 ms

UWB-OFDM

WiMedia Alliance

ECMA-368

There has been a lot of interest in ultra-wideband communications, in the past few years, for short range (less than a few meters) communications of hundreds of megabits per second. As part of the IEEE 802.15 discussions, the UWB-OFDM technique was suggested.

Because of industrial political conflicts, an “outside group” was formed which continues to push the idea of UWB-OFDMA. This organization was originally called the Multiband OFDM Alliance (MBOA) and eventually became known as the WiMedia Alliance (www.wimedia.org). They are promoting the communications concept known as UWB-OFDM. This concept is described on the next few pages.

The basic concept is for each user to frequency-hop over a very wide band of approximately one and a half GHz , and transmit at data rates up to 480 Mbps.

UWB-OFDM

Wi-Media Alliance- ECMA-368

Fourteen Bands

3.1 GHz-10.1 GHz

## Center Frequency of Band #1=3.432GHz

## Center Frequency of Band #14=10.298GHz

Bandwidth of Each Band=528 MHz

Channel Spacing ((f) =4.125 MHz

## Number of Tones / Band= 128

Number of Data Tones/ Band=100

Number of Pilot Tones/ Band=12

Number of Guard Tones/ Band=10

Number of Null Tones=6

Tblock=1/(f=1/4.125 MHz=242.42 ns

Number of Samples in Zero-Padded Suffix=37 (70.08 ns)

Total Block Time= 242.42+70.08=312.5 ns

Rblock=3.2 Mblocks/sec

Bit Rates: 53.3Mbps, 80 Mbps, 106.7 Mbps, 160 Mbps, 200Mbps, 320 Mbps, 400 Mbps and 480 Mbps

Modulation: QPSK

Codes: r=1/3, 1/2, 5/8, 3/4 and k=9

Range:  5 meters

Frequency Hopping Structure

ECMA-368

Three Bands

frequency

IFFT Output       Zero-Padded

(OFDM Symbol)           Suffix

ECMA Standard-368

First Edition-December 2005

Tsym=Symbol length

Npacket=Number of symbols in packet

fc(m)=Center frequency of m th band

q(n)=Function that maps the n th symbol to the appropiate

frequency band

sn(t)=Complex baseband representation of n th symbol

sn(t)=0 for t [0, Tsym]

Exact structure of n th symbol depends on its location within the packet

##### ND

##### sn[k]=1/(NFFT[ (CD,n[l]ej2(MD[l]k/NFFT

l=0

##### NG

##### +  (CG,n[l]ej2(MG[l]k/NFFT

l=0

##### NP

##### + (CP,n[l]ej2(MP[l]k/NFFT]

l=0

##### ND=Number of data subcarriers

##### NG=Number of guard subcarriers

##### NP=Number of pilot subcarriers

# Text boxes

4

5

6

7

8

9

10

11

12

1

2

3

13

14

Symbol

3168MHz

Band #1

Band #2

3696 MHz

4224 MHz

Band #3

4752 MHz

Npacket-1

sRF(t)= Re {ej2(f0t ( sn(t-nTsym)ej(fc(q(n))t }

n=0