EE4303 Spring 2002

Homework #6 (due April 11 2002):

Take the 0.5um CMOS opamp example from the notes and perform the following design steps and simulations:

- Change IBIAS to 150uA, but do not change any of the transistor sizes.

- Change CLOAD to 5pF

Then,

  - Simulate the DC operating point of the opamp; report node voltages and transistor operating conditions

  - Change the value of the compensation capacitor CC to have a phase margin of 60 degrees.

  - Simulate the AC open loop response of the opamp (i.e. the loop gain for a unity feedback configuration). Report the DC gain, the first pole frequency, the unity gain frequency and phase margin, and the phase crossover frequency and gain margin.

  - Put the OpAmp in a unity gain follower configuration and simulate the transient step response for a step input of from 1.5V to 1.6V, 1.5V to 1.4V, 1.5V to 2.5V and 1.5V to 0.5V etc.). Report graphs for each of the 4 stepresponses (i.e. plots of v(out) versus time).